## Slide 1: Electronic Devices
10th ed., Global Edition
Chapter 8
Field-Effect Transistors
(FETs)

## Slide 2: Electronic Devices
10th ed.
◆ Discuss the JFET and how it differs from the BJT
◆ Discuss, define, and apply JFET characteristics and
parameters
◆ Discuss and analyze JFET biasing
◆ Discuss the ohmic region on a JFET characteristic curve
◆ Explain the operation of MOSFETs
◆ Discuss and apply MOSFET parameters
◆ Describe and analyze MOSFET bias circuits
◆ Discuss the IGBT
◆ Troubleshoot FET circuits
Objectives:

## Slide 3: Electronic Devices
The JFET
The JFET (or Junction Field Effect Transistor) is a normally ON device. For the n-channel device illustrated, when the drain is positive with respect to the source and there is no gate-source voltage, there is current in the channel.
When a negative gate voltage is applied to the FET, the electric field causes the channel to narrow, which in turn causes current to decrease.

## Slide 4: Electronic Devices
The JFET
As in the base of bipolar transistors, there are two types of JFETs: n-channel and p-channel. The dc voltages are opposite polarities for each type.
The symbol for an n-channel JFET is shown, along with the proper polarities of the applied dc voltages. For an n-channel device, the gate is always operated with a negative (or zero) voltage with respect to the source.
Gate
Source
Drain

## Slide 5: Electronic Devices
The JFET
There are three regions in the characteristic curve for a JFET as illustrated for the case when VGS = 0 V.
Between A and B is the Ohmic region, where current and voltage are related by Ohm’s law.
Ohmic region

## Slide 6: Electronic Devices
Active region
(constant current)
The JFET
There are three regions in the characteristic curve for a JFET as illustrated for the case when VGS = 0 V.
From B to C is the active (or constant-current) region where current is essentially independent of VDS.
Between A and B is the Ohmic region, where current and voltage are related by Ohm’s law.

## Slide 7: Electronic Devices
The JFET
There are three regions in the characteristic curve for a JFET as illustrated for the case when VGS = 0 V.
Beyond C is the breakdown region. Operation here can damage the FET.
Breakdown
From B to C is the active (or constant-current) region where current is essentially independent of VDS.
Between A and B is the Ohmic region, where current and voltage are related by Ohm’s law.

## Slide 8: Electronic Devices
The JFET
As VGS is varied, a family of characteristic curves is developed that shows the relationship between VDS, ID and VGS.
The characteristic curves for an n-channel device are illustrated. Notice that Vp is positive and has the same magnitude as VGS(off).
Note that he pinch-off voltage varies with VGS.

## Slide 9: Electronic Devices
The JFET
A plot of VGS to ID is called the transfer or transconductance curve. The transfer curve is a is a plot of the output current (ID) to the input voltage (VGS).
The transfer curve is the graphical representation of the equation:
By substitution, you can find other points on the curve for plotting the universal curve.
IDSS
2
0.3 VGS(off)
0.5 VGS(off)
IDSS
4

## Slide 10: Electronic Devices
The JFET - Example
A certain 2N5458 JFET has IDSS = 6.0 mA and VGS(off) = – 3.5 V.
Example:
(a) Show the values of the these end points on the transfer curve.
= 6.0 mA
= -3.5 V

## Slide 11: Electronic Devices
The JFET - Example
A certain 2N5458 JFET has IDSS = 6.0 mA and VGS(off) = – 3.5 V.
Example:
(a) Show the values of the these end points on the transfer curve.
(b) Show the point for the case when ID = 3.0 mA.
= 6.0 mA
= -3.5 V
(b) When ID = ½ IDSS, VGS = 0.3 VGS(off). Therefore, VGS = -1.05 V
Solution:
-1.05 V
3.0 mA

## Slide 12: Electronic Devices
The JFET
The transconductance is the ratio of a change in output current (DID) to a change in the input voltage (DVGS).
The following approximate formula is useful for calculating gm if you know gm0.
DID
DVGS
The value of gm0 can be found from
This definition is

## Slide 13: Electronic Devices
The JFET - Example
Because the slope changes at every point along the curve, the transconductance is not constant, but depends on where it is measured.
Example:
What is the transconductance for the JFET at the point shown?
5.7
3.7
-0.7
-1.3
Solution:
3.33 mS

## Slide 14: Electronic Devices
The JFET - Example
The input resistance of a JFET is given by:
Example:
Compare the input resistance of a 2N5485 at 25 oC and at 100 oC. The specification sheet shows that for VGS = -20 V, IGSS – 1 nA at 25 oC and 0.2 mA at 100 oC.
Solution:
At 25 oC,
where IGSS is the current into the reverse biased gate.
20 GW!
JFETs have very high input resistance, but it drops when the temperature increases.
At 100 oC,
100 MW

## Slide 15: Electronic Devices
JFET Biasing - Examplw
Self-bias is simple and effective, so it is the most common biasing method for JFETs. With self bias, the gate is essentially at 0 V.
An n-channel JFET is illustrated. The current in RS develops the necessary reverse bias that forces the gate to be less than the source.
Example:
Assume the resistors are as shown and the drain current is 3.0 mA. What is VGS?
= +12 V
1.5 kW
330 W
1.0 MW
Solution:
VG = 0 V; VS = (3.0 mA)(330 W) = 0.99 V
VGS = 0 – 0.99 V =
- 0.99 V

## Slide 16: Electronic Devices
JFET Biasing - Example
You can use the transfer curve to obtain a reasonable value for the source resistor in a self-biased circuit.
Example:
What value of RS should you use to set the Q point as shown?
Solution:
375 W
Q
The Q point is approximately at ID = 4.0 mA and VGS = -1.25 V.

## Slide 17: Electronic Devices
JFET Biasing
Voltage-divider biasing is a combination of a voltage-divider and a source resistor to keep the source more positive than the gate.
VG is set by the voltage-divider and is independent of VS. VS must be larger than VG in order to maintain the gate at a negative voltage with respect to the source.
Voltage-divider bias helps stabilize the bias for variations between transistors.

## Slide 18: Electronic Devices
JFET Biasing
A graphical analysis of voltage-divider biasing is illustrated. A typical transconductance curve for the 2N5485 is shown with IDSS = 6.5 mA and VGS(off) = -2.2 V.
VG = 2.79 V
VG/RS = 2.79 mA
2.79 V
Start with VG:

## Slide 19: Electronic Devices
JFET Biasing
A graphical analysis of voltage-divider biasing is illustrated. A typical transconductance curve for the 2N5485 is shown with IDSS = 6.5 mA and VGS(off) = -2.2 V.
VG = 2.79 V
VG/RS = 2.79 mA
2.79 V
Connect the points to establish the load line.
Q
Start with VG:
The Q-point is read from the plot. It is 3.3 mA and -0.7 V.

## Slide 20: Electronic Devices
JFET Biasing
An even more stable form of bias is current-source bias. The current-source can be either a BJT or another FET. With current-source biasing, the drain current is essentially independent of VGS.
In this circuit Q2 serves as a current source for Q1. An advantage to this particular circuit is that the output can be adjusted (using RS2) for 0 V DC.

## Slide 21: Electronic Devices
JFET Ohmic Region
As described before, the ohmic region is between the origin and the active region. A JFET operated in this region can act as a variable resistor.
Data from an actual FET is shown. The slopes (which represent conductance) of successive VGS lines are different in the ohmic region. This difference is exploited for use as a voltage controlled resistance.
Ohmic region

## Slide 22: Electronic Devices
JFET Ohmic Region
When used as a variable resistor, the load line is set to intersect in the Ohmic region. The value of RDS varies depending on which VGS curve is intersected. Notice that the ohmic region extends into the third quadrant, so zero bias is an option.

## Slide 23: Electronic Devices
JFET Ohmic Region
Here is a circuit in which the JFET is used as a variable resistor. Notice that that the drain is connected through a capacitor, which means the JFET’s Q-point is at the origin.
The gain of the BJT depends on the dc voltage setting of VGG.

## Slide 24: Electronic Devices
The MOSFET
MOSFETs are another type of field-effect transistor in which the gate is insulated from the channel by a silicon dioxide layer. The D-MOSFET has a channel that is controlled by applying a gate voltage and comes as either an n-channel or a p-channel device.
For an n-channel type, a negative voltage depletes the channel (D-mode); a positive voltage enhances the channel (E-mode).
D-MOSFETs can operate in either mode.
D-MOSFET
operating in D-mode
operating in E-mode

## Slide 25: Electronic Devices
The MOSFET
The E-MOSFET differs from the D-MOSFET in that in has no structural conduction channel. A channel is induced by the application of a gate voltage. E-MOSFETs can only operate in enhancement mode.
Induced channel
With no gate voltage, there is no channel.
For an n-channel type, a positive voltage applied to the gate induces a conduction channel.

## Slide 26: Electronic Devices
MOSFET Symbols
MOSFET symbols are shown. Notice the broken line representing the E-MOSFET that has an induced channel. The n channel has an inward pointing arrow.
n-channel p-channel
E-MOSFETs
n-channel p-channel
D-MOSFETs

## Slide 27: Electronic Devices
The MOSFET
Question:
Why can’t an E-MOSFET operate in depletion mode?
Answer:
There is no conduction channel in depletion mode.
Follow-up:
What polarity is required on the gate of a p-channel E-MOSFET to cause a conduction channel to be induced?.
Answer:
Negative.

## Slide 28: Electronic Devices
Power MOSFETs
MOSFETs are widely used in power applications. One structure is a large array of low-power MOSFETs that are connected in parallel and act as one. By selecting matched MOSFETs with a negative temperature coefficient, thermal runaway is avoided.
Another structure has the insulated gate in the shape of a V or U. VMOSFETs and UMOSFETs are designed for power handling by creating a shorter and wider channel that can handle higher current.
VMOSFET structure

## Slide 29: Electronic Devices
Dual-Gate MOSFETs
The dual-gate MOSFET has two gates, which have advantages in certain applications. The schematic symbol for an n-channel depletion and an n-channel enhancement mode device is shown. Dual-gate devices are useful in high-frequency RF amplifiers and in certain automatic gain control (AGC) circuits.
Dual-gate D-MOSFET symbol Dual-gate D-MOSFET symbol

## Slide 30: Electronic Devices
The E-MOSFET Transfer Curve
The transfer curve for a MOSFET is has the same parabolic shape as the JFET but the position is shifted along the x-axis. The transfer curve for an n-channel E-MOSFET is entirely in the first quadrant as shown.
The curve starts at VGS(th), which is a nonzero voltage that is required to have channel conduction. The equation for the drain current is
Transfer curve for E-MOSFET

## Slide 31: Electronic Devices
The D-MOSFET Transfer Curve
Recall that the D-MOSFET can be operated in either mode. For the n-channel device illustrated, operation to the left of the y-axis means it is in depletion mode; operation to the right means is in enhancement mode.
As with the JFET, ID is zero at VGS(off). When VGS = 0, the drain current is IDSS, which for this device is not the maximum current. The equation for drain current is
Transfer curve for D-MOSFET

## Slide 32: Electronic Devices
MOSFET Handling
MOSFETs require special handling; see text for details. Summarizing these handling requirements:
  MOSFETs are static sensitive and are shipped in special conductive foam or conductive bags. If there is wire ring around the leads, it is removed prior to installation.
  All instruments and metal benches used in assembly or test should be connected to earth ground.
  The assembler’s or handler’s wrist should be connected to a commercial grounding strap, which has a high-value series resistor for safety.
  MOSFETs should not be removed from a circuit that has power on.
  Signals should not be applied to a MOS device while the dc power supply is off.

## Slide 33: Electronic Devices
MOSFET Handling
Question:
Why is it necessary to have a high value resistor in series with a grounding strap?
Answer:
In case the user contacts an electrical source, the high value resistor limits the current that can flow through the body, avoiding a dangerous shock.

## Slide 34: Electronic Devices
MOSFET Limiting Parameters
All transistors have limits of operation; see text for details of MOSFET limiting parameters. Summarizing these parameters:
  Drain Source Breakdown Voltage, V(BR)DSS, is the voltage that will do irreparable damage if it is exceeded between drain and source).
  Blocking voltage, BVDSS, is maximum drain to source voltage that can be applied to the MOSFET.
  On-resistance, RDS(on), is the ratio of drain voltage to drain current. Continuous drain current, ID, is the maximum current that can safely be carried by a FET continuously.
  Power dissipation, PD, is the maximum power allowed for safe operation and is based on junction to case temperature.

## Slide 35: Electronic Devices
E-MOSFET Biasing
E-MOSFETs can be biased using bias methods like the BJT methods studied earlier. Voltage-divider bias and drain-feedback bias are illustrated for n-channel devices.
Voltage-divider bias Drain-feedback bias

## Slide 36: Electronic Devices
D-MOSFET Biasing
The simplest way to bias a D-MOSFET is with zero bias. This works because the device can operate in either depletion or enhancement mode, so the gate can go above or below 0 V.
Zero bias, which can only be used for the D-MOSFET

## Slide 37: Electronic Devices
The IGBT
The IGBT is a device that has the output conduction characteristics of a BJT but is voltage controlled like a MOSFET; it is an excellent choice for many high-voltage switching applications. The IGBT has three terminals: gate, collector, and emitter. It has the input characteristics of a MOSFET (very high input impedance)
and BJT output characteristics. It is mainly used in high voltage (>1000 V), medium-frequency switching applications such as in motor control.

## Slide 38: Electronic Devices
Selected Key Terms-1
JFET
Drain
Source
Gate
Junction field-effect transistor; one of two major types of field-effect transistors.
One of three terminals of a FET analogous to the collector of a BJT.
One of three terminals of a FET analogous to the emitter of a BJT.
One of three terminals of a FET analogous to the base of a BJT.

## Slide 39: Electronic Devices
Selected Key Terms-2
Transconductance (gm)
MOSFET
Depeletion
Enhancement
The ratio of a change in drain current to a change in gate-to-source voltage in a FET.
Metal oxide semiconductor field effect transistor; one of two major types of FETs; sometimes called IGFET.
In a MOSFET, the process of removing or depleting the channel of charge carriers and thus decreasing the channel conductivity.
In a MOSFET, the process of creating a channel or increasing the conductivity of the channel by the addition of charge carriers.

## Slide 40: Electronic Devices
Quiz Q1
1. If an n-channel JFET has a positive drain voltage and the gate-source voltage is zero, the drain current will be
a. zero
b. IDSS
c. IGSS
d. none of the above

## Slide 41: Electronic Devices
Quiz Q2
2. For a JFET, two voltages with the same magnitude but opposite signs are
a. VD and Vp
b. VD and VS
c. VGS(th) and Vcutoff
d. Vp and VGS(off)

## Slide 42: Electronic Devices
Quiz Q3
3. A set of characteristic curves for a JFET are shown. The blue lines represent different values of
a. VDS
b. VGS
c. VS
d. VTH

## Slide 43: Electronic Devices
Quiz Q4
4. Transconductance can be expressed as
a.
b.
c.
d.

## Slide 44: Electronic Devices
Quiz Q5
5. Q1 is biased using
a. self-bias
b. voltage-divider bias
c. current-source bias
d. zero bias

## Slide 45: Electronic Devices
Quiz Q6
6. The JFET operating point in the circuit shown is
a. at the origin
b. at Isat
c. at VCC
d. undefined

## Slide 46: Electronic Devices
Quiz Q7
7. The JFET in this circuit acts like a(n)
a. voltage source
b. amplifier
c. capacitor
d. resistor

## Slide 47: Electronic Devices
Quiz Q8
8. The symbol shown is for
(a) an n-channel D-MOSFET
(b) a p-channel D-MOSFET
(c) an n-channel E-MOSFET
(d) a p-channel E-MOSFET

## Slide 48: Electronic Devices
Quiz Q9
9. The transfer curve shown is for an n-channel
a. E-MOSFET
b. D-MOSFET
c. JFET
d. all of the above

## Slide 49: Electronic Devices
Quiz Q10
10. The symbol shown is for
a. an IGBT
b. a D-MOSFET
c. an E-MOSFET
d. a JFET

## Slide 50: Electronic Devices
Answers
Answers:
1. b
2. d
3. b
4. a
5. c
6. a
7. d
8. d
9. a
10. a